## Slide 1
Machine Learning for Thermal Soaring
Autonomously mimic the soaring habits of birds with a glider
Travis Crumley, David Egolf, and Garrett Wilson
Edward F. Cross School of Engineering, Walla Walla University, College Place, Washington
REFERENCES
Allen, Michael J. "Autonomous soaring for improved endurance of a small uninhabited air vehicle." Proceedings of the 43rd aerospace sciences meeting, AIAA. 2005.
Edwards, Daniel J. Autonomous Locator of Thermals (ALOFT) Autonomous Soaring Algorithm. No. NRL/FR/5712--15-10. NAVAL RESEARCH LAB WASHINGTON DC, 2015.
Korb, Kevin B., and Ann E. Nicholson. Bayesian Artificial Intelligence. Boca Raton, FL: CRC, 2010. Print.
Lawrance, Nicholas RJ. Autonomous soaring flight for unmanned aerial vehicles. Diss. University of Sydney, 2011.
A
B
ABSTRACT
Our project to create and implement the software necessary for a glider to autonomously find and use the updrafts from thermals to sustain longer flight times was divided into three parts: a basic implementation of existing algorithms, an exploration of thermal identification methods, and an exploration of machine learning to provide better soaring decisions.
IMPROVEMENT: THERMAL IDENTIFICATION
The centroid method merely provides an estimate of where the thermal center may be. One improvement upon this method would be to predict what the entire thermal looks like. We investigated two possible approaches: Bayesian parameter estimation, which predicts a probability distribution over possible values each parameter of a model could take on, and Gaussian process regression, which predicts a Gaussian probability distribution over values each point in a -dimensional space could take on. Because of its superior predictions and execution speed in tests, Gaussian process regression was pursued further and implemented in simulation.
Figure 3: Gaussian process regression (left) run live on data collected from a glider flying in the simulator (right)
SUMMARY
Success!!!
In partial fulfillment of the requirements for ENGR 498, Senior Seminar
RESULTS. As the glider flies a flight path gaining altitude, it collects and runs the last 45 seconds of data through Gaussian process regression predicting the vertical velocity in a 20-meter radius around the glider. Because it predicts a probability distribution, which provides a measure of uncertainty, this can be used in determining whether it is beneficial to latch onto a thermal. The glider will start circling the point of the highest predicted vertical velocity if with 85 percent confidence this velocity is above a certain threshold. Figure 3 shows a test in simulation where the glider successfully found a thermal and has orbited it twice.
INTRODUCTION
The 13-acre property where the structure is to be built is located about five miles south of College Place, WA in Walla Walla County. The relative terrain is mostly flat with a few trees and a small river, the East Walla Walla River, passing through the property. However, some 40 foot bluffs unique to the Walla Walla Valley are within 1,500 feet of the proposed building site. A grass landing strip bisects the property diagonally (See Figure 1.)
Figure 1: Senior Project Site (Google Earth)
The specified dimensions are 40 feet by 60 feet by 12 feet tall with a roof slope of 3 in 12. The airplane door is 40 foot by 10 foot. Five moment frames providing resistance to transverse direction loads are evenly spaced along the 60 foot dimension. Connecting beams and tension-only braces transfer longitudinal loadings to the foundation.
IMPROVEMENT: POLICY DEVELOPMENT
OVERVIEW OF METHODS EXPLORED: Under the centroid method, the UAV circles the estimated thermal center at a fixed radius. One improvement on this method is to develop strategies for extracting energy from the thermal that are more flexible. We investigated three approaches to achieve this with machine learning: tabled-based Q learning, neural fitted Q learning, and dynamic programming with neural interpolation. Tabled-based Q learning discretizes the state space, and develops estimates for the value of performing each possible action in each discretized chunk using Q learning. We used this method successfully in a highly idealized setting, but we had some difficulty in using it to scale it up. Future work could include focusing on variable chunking size, allowing for better scaling. Neural-fitted Q learning also uses Q learning, but stores value estimates using a neural network. We had only limited success with this method, and future work would focus on incorporating new information into a neural network without losing the old information stored. Dynamic programming with neural interpolation is a model based method, using a model of the system to carry out dynamic programming. To allow for a continuously varying policy, the value estimates and policy estimates are both stored in neural networks.
Figure 3: Example of RISA’s Output
RESULTS: We had the most success using dynamic programming with neural interpolation. A plausible and flexible policy was developed that adjusts to thermal position and shape. State variables used were: position from center of thermal, height of UAV, and direction of UAV. Current work is focused on testing the algorithms developed in the more sophisticated ccrcsim simulator.
Figure 4: Value and policy estimates with thermal at 5. In the policy plot, blue = travel towards origin, green = travel away from origin, and red = orbit.
Figure 2: Gaussian process regression (center) compared with Bayesian parameter estimation (right) learning what a simple Gaussian-shaped thermal model looks like given only discrete points along a circular flight path (left)